VUBug:  AN M68000 MONITOR PROGRAM                      I.  Introduction.                         VUBug is a primitive single user monitor program designed           to interface the user to the "Raymatic" M68000 development board           designed by Raymond Carr at Vanderbilt University in 1988.  The          monitor program itself was originally written by Edward M. Carter          also while at Vanderbilt in 1983.  This documentation relates to          the 1988 version of the program, about two thirds of which is new.          The new stuff was added by Russell G. Brown, then of Vanderbilt, but          lately of Cornell Computer Science.  It allows the user to perform          such operations as are necessary to develop and debug M68000          assembly programs in conjunction with a host computer running           an M68000 assembler which is capable of generating object code in          the Motorola S-record format.  Some functions provided by VUBUG           are load from host, dump memory, disassemble memory, and run at           address.  Feel free to distribute this source and documentation,          but make sure that the copyright and like information stays on it.          Also, please make sure that any modified version of this program          which you may distribute is obviously marked as being modified.                    II.  Running VUBug                         VUbug comes up running as soon as power is applied to the           system.  It asserts its presence by printing the following           message:                         M68000 Monitor VUBug Version 4.0 27 April, 1988                                   !_                    If there is anything wrong with the system RAM, it will instead           respond                         RAM Error!!!!                    Assuming that a RAM error doesn't happen, you can now begin           entering commands.                    III.  Getting Started                         The first thing that you will want to do is to load and           execute an assembly language program using VUBug.  The following           is an example interactive execution session:                    1.   Turn on the system.  The VUBug boot message prints at the                terminal.          2.   Type 'e'.  VUBug responds "Terminal Mode:".          3.   Log into the host system.  Enter vi and type in the               following program:                        org     $4400                        move.l  #$00000004,d0                        movea.l #$000019ca,a3                        adda.w  d0,a3                        move.l  a3,d0                        trap    #$06                        trap    #$0                        end                     4.   Write and quit from vi.  Assemble the program by           typing                         mas68k -l <progname>.               where progname is the name of your sample program. 5.             Examine the listing file produced by mas68k to see the source                and object code together.  The listing file is called               <progname.l>.          6.   Type 'cat <progname.o>' but DO NOT! type a carriage return.          7.   type ctrl-L.  VUBug will exit terminal mode, feed a               carriage return to the host, and accept an Srec format object               file.          8.   You are now back in VUBug.  Type 'a 4400'.  You will see an               assembly listing which is equivalent to your source code,               except that it has values substituted for all labels.  There               will be a number of garbage lines following the program.               disregard these.          9.   Type 'g 4400'.  This is the command meaning "go at $4400".               VUBug responds with the following:                        Program:                        000019ce                        !               This is approximately how all debugging sessions should          begin.  Once you have become more familiar with VUBug, you will          learn shortcuts and enhancements, but the commands already used          will serve for a start.          IV.  VUBug Commands               This section contains the full, alphabetic listing of the           commands provided in VUBug.  For information on how to get help           for commands while in VUBug, see the section on 'h'.                                     A - Assembly Listing                              A provides a source code listing of memory locations                specified in one of the following ways:                                       A<cr>           List 20 instructions from last                                         examined address.                         A xxxx          List 20 instructions from address                                         xxxx.                         A xxxx,yyyy     List from xxxx to yyyy.               B - Set/Remove Breakpoints                               B permits the setting and removing of breakpoints in a user                program.  B is invoked as follows:                                       B<cr>           List all breakpoints.                        B+xxxx          Add a breakpoint at address xxxx.                         B-xxxx          Remove a breakpoint at xxxx.                         B#              Remove all breakpoints.                                                            C - Copy Memory                               C allows the copying of a data block from one location to                another.  It is called using:                                       C xxxx=yyyy,zzzz.                              This copies memory from a block which starts at yyyy and                ends at zzzz to a block starting at xxxx.  NOTE:  the copy                routine works from bottom to top.  Therefore care must be                taken when copying between blocks that share address space.                                                            D - Dump Memory                D is used to provide a hex dump of memory.  Memory is                printed out in lines consisting of an address, 16 hex                values, and the ascii representation of such of those                values as have printable characters.  The format for                calling D is as follows:                                        D<cr>           Dump 64 bytes from last examined                                         location.                        D xxxx          Dump 64 bytes from xxxx.                        D xxxx,yyyy     Dump bytes from xxxx to yyyy.                                                            E - Enter terminal emulator mode                              When E is entered, VUBug enters a passthrough mode in which                any key entered at the keyboard is passed through to the                host, and vice versa.  This is true for all characters                except for ctrl-X, which causes VUBug to exit terminal                emulator mode, and ctrl-L, which is the same as ctrl-X,                except that it causes VUBug to enter load mode.  E is                invoked as follows:                                       E<cr>               G - Start user program                              G is the VUBug command to start a user program running.  A                user program which is properly designed to end will have as                its last executed line                                       trap    #$00                               G is called in one of the following ways:                                       G<cr>           Go from start address in the last                                         executed L command.                        <cr>            Same as G<cr>.                         G xxxx          Go from address xxxx.                                                            H - Print help messages.                              H is used to print a simple message (consisting mostly of                instruction syntax) to the terminal.  It is called with:                                       H<cr>           Prints a list of commands for                                         which help is available.                         Hx              Prints the long help message for                                        command x.  If x is nonexistant,                                        Hx acts like H<cr>.                                                            L - Load user program from host                              L causes VUBug to accept an S-record format object file                from the host.  It is called in one of the following ways:                                       L<cr>           Load from host with no offset.                        ctrl-L          Same as L<cr> but invoked from                                         emulator mode.                        L xxxx          Load from host with offset xxxx.               M - Enter memory update mode                              M invokes a submode of VUBug in which modifications to                memory locations can be made.  M is invoked as follows:                                       M<cr>           Start memory mode.                         M xxxx          Start memory mode at xxxx.                Memory mode subcommands are the following:                                       .xxxx           Set pointer to location xxxx.                        =xx             Update current location to xx.                        ,xx             Increment pointer, then update.                        +               Increment pointer.                        -               Decrement pointer                        <cr>            Print current pointer and value.                              Typing any other character in memory update mode causes an                exit back into VUBug proper.                                                            P - Prototype commands in RAM                              P allows the user to create new command subroutines in RAM                and call them without having to burn new ROMs.  This is                significant in that ordinarily user programs cannot make                use of the interrupt routines and other subroutines                provided in VUBug.  P is set up to allow a user routine to                make use of these subroutines.  It is invoked as follows:                                       Px xxxx         Load address xxxx for prototype                                         command x.                        Px<cr>          Execute prototype command x.                              Note that x must be a 1, 2, or 3.               R - Enter register examine/update mode                              R invokes a submode of VUBug in which registers may be                examined and changed.  It is called in the following way:                                       R<cr>           Start register mode.                        R xx            Start mode at register xx,                                         where xx is one of:                                                SR/_sr - status register,                                                 PC/_pc - program counter,                                                 dx - data register 0 - 7,                                                 ax - address reg. 0 - 7.                              Register examine/update commands are as follows:                                       .xx             Set pointer to register xx.                         =xxxxxxxx       Set current register to xxxxxxxx.                         <cr>            Print all registers.                              Any other character entered in register submode causes an                exit to VUBug.                                                            S - Single step mode                              In single step mode, a Go command causes VUBug to execute a                single instruction and then return to the prompt, allowing                registers to be examined and changed between instructions.                S is called in one of two ways:                                       S+              Turn on single step mode.                         S-              Turn off single step mode.                                                            T - Trace mode                              In trace mode, a Go command causes VUBug to execute a                program, printing out the PC after each instruction.  This                permits tracing of a program's path.  It is called as                follows:                                       T+              Turn on trace mode.                        T-              Turn off trace mode. V.                  U - Upload user program from terminal               U allows VUBug to upload an S-record format object file               from the terminal.  This allows the user to connect the               68000 board to a microcomputer, using it as both terminal               and host.  Upload is invoked with one of the following               commands:                        U<cr>           Upload from terminal with no offset.                        U xxxx          Upload from terminal with offset xxxx.          V.   Troubleshooting                          There is not a whole lot that can go wrong with VUBug.            Most of the possible difficulties actually have their roots in           hardware.  If a RAM error is indicated at boot-up time, then one           of the system RAM chips needs replacing.  If no boot-up message           is printed, then something is wrong with one of the following:            the terminal, the terminal cable, the ACIAs on the development           board, the system RAM, or the VUBug ROM.                         If an error is found in VUBug's performance, the thing to           do is to document carefully when and where the bug appears, and           report the problem to the nearest digital electronics professor.                              VI.  Caveats               A number of things should be taken into account when using          VUBug.  Most of these have to do with the memory map.  Number          one is that hitting the reset button invokes the RAM test program          which CLEARS THE RAM!  For this reason, ctrl-C should be used to          recover control from a lost program.               The memory map for the board looks like this:                        0000 - 3FFF     System ROM                        4000 - 43FF     System RAM                        4400 - 7FFF     User RAM                        8000 - 803E     PI/T (68230) registers EVEN ONLY!                        A000            Load Port Status Register                        A002            Load Port Data Register                        C000            Terminal Port Status Register                        C002            Terminal Port Data Register               Note that the PI/T and ACIA registers are on even only          locations.  Attempting to write to a peripheral chip on an odd          location will lock up the system.  Similarly, writing to system          RAM can cause unexpected results, up to and including locking          up the system.          VII. Conclusion                         VUBug 4.0, mas68k, and the Raymatic development board form           an effective development environment for M68000 assembly           language programs.  While they cannot substitute for           professional development/analysis systems, it is nevertheless           possible to complete considerable software endeavors with a           reasonable minimum of difficulty.